Occupancy Inspection Requirements for the

Village of Lawrence

SMOKE ALARMS THROUGHT THE HOME/BUSINESS:

- One in or near the kitchen

- One in basement

- One in garage if attached

- One in each hallway

- One in each bedroom (recommended)

- One in living room

- One in the hallway going upstairs

FIRE EXTINGUISHERS: (ABC all purpose & up to date on charge)

- One in the kitchen but not near the stove

HAND RAILS:

- One going upstairs

- One going into the basement

DROP PIPE ON HOT WATER HEATER:

- The hot water heater has a safety relief valve either on the top or the side of unit. This pipe must extend to within 6 inches of the floor.  In a mobile home it should extend through the floor under the trailer.

ELECTRICAL:

- All outlets on the walls must have a cover

- Electric service panel must have a cover

- Any wire connections boxes must have a cover

- No wires are to be exposed or hanging loose out of the ceiling lights or wall outlets

- Outlets in the kitchen or bathrooms near water must have ground fault receptacle’s if home is wired with two wires plus a ground.

PLUMBING:

- Stools, sinks, drains. Must all work

BUILDING DEFICIENCIES:

- No broken windows, holes in the floors, walls or doors

- Siding must cover home

- Carpets should not have holes or tears